## Slide 1
BandWeave: Enhanced Channel Estimation in
MIMO Networks with Multi-Band Fusion
(Best Paper INFOCOM-2026)
K Foysal Haque*, Francesca Meneghello*, Jonathan Ashdown†, Francesco Restuccia*
*Institute for Intelligent Networked Systems, Northeastern University, Boston, USA
†Spectrum AI Solutions, USA

## Slide 2: AR/VR: Shaping the Future of Interactions
We are very far from truly seamless and immersive
AR/VR experiences
1. Precedence Research. "Spatial Computing Market Size, Share, Trends, Analysis Report, 2025-2034." Accessed October 21, 2025. https://www.precedenceresearch.com/spatial-computing-market
Global market value is predicted to reach 1066 Billion by 2034 [1]

## Slide 3: What is the Current Bottleneck?
Object recognition​
Semantic segmentation
Compute-intensive
AI/ML tasks
120 Hz frame rate and 8K resolution are needed! [1]
1. M Gallagher, ER Ferrè, "Cybersickness: a multisensory integration perspective", Multisensory Research, 2018. Ars Technica, "Virtual Perfection: Why 8K resolution per eye isn't enough for perfect VR", 2013.
Meta Quest 3 (1.5-2 hours)
Weight
515 grams
Apple Vision Pro (Up to 2 hours)
Weight
650 grams plus
353 grams battery

## Slide 4: Wireless Edge Computing For Next-Gen App
Offload compute intensive task to edge server
Edge Devices
Wireless Link
Edge Server
120 Hz @ 8K → 40 Gbps → Wi-Fi supports 1.2 Gbps
1. M Gallagher, ER Ferrè, "Cybersickness: a multisensory integration perspective", Multisensory Research, 2018. Ars Technica, "Virtual Perfection: Why 8K resolution per eye isn't enough for perfect VR", 2013.

## Slide 5: Channel-Estimation– the Key Enabler of MIMO
Accurate channel estimation enables spatial multiplexing
and interference mitigation in MIMO systems
Multi-path superposition
Destructive interference
Degraded Channel estimation
Hamper Communication

## Slide 6: Analyzing CFR at Different Center Freq.
CFR is band-specific
Multipath components are band-independent
CIRs from different center frequencies exhibit consistent dominant multi-paths
Diff. bands provide complementary views of the same instances

## Slide 7: BandWeave: Enhanced Ch. Est. with Band Fusion
BandWeave
Beamformer
BandWeave
Beamformee
Pilots for Band
1, 2… NB
Feedback from Fused Ch.
- Estimate Precoding Matrix
Beamformed Data
-Est. Ch. Response for
Bands 1 to NB
- Fuse Responses in Time Domain
BandWeave  Enhanced Ch. Est.  Improved Comm.

## Slide 8: Prior Work and Existing Challenges
A. Banerjee, X. Zhao, V. Chhabra, K. Srinivasan, and S. Parthasarathy, “HORCRUX: Accurate Cross Band Channel Prediction,” in Proceedings of the 30th Annual International Conference on Mobile Computing and Networking, pp. 1–15, 2024.
M. S. Safari, V. Pourahmadi, and S. Sodagari, “Deep UL2DL: Data-driven Channel Knowledge Transfer from Uplink to Downlink,” IEEE Open Journal of Vehicular Technology, vol. 1, pp. 29–44, 2019.
X. Li, H. Wang, Z. Chen, Z. Jiang, and J. Luo, “UWB-Fi: Pushing Wi-Fi Towards Ultra-Wideband for Fine-Granularity Sensing,” in Proceedings of the 22nd Annual International Conference on Mobile Systems, Appli-cations and Services, pp. 42–55, 2024
J. Pegoraro, J. O. Lacruz, M. Rossi, and J. Widmer, “HiSAC: High-Resolution Sensing with Multiband Communication Signals,” in Proceedings of the 22nd ACM Conference on Embedded Networked Sensor Systems, pp. 549–563, 2024.
Cross Link CFR Estimation
Cross Band CFR Estimation
Spectrum Splicing
UL CFR
Predicted DL CFR
Prior work focuses only on sensing or CFR prediction and does not improve estimation fidelity

## Slide 9: Summary of Key Contributions
BandWeave is the first framework to coherently
fuse CFRs to enhance channel estimation resolution
We extensively evaluate BandWeave with an IEEE 802.11ac MU-MIMO and a 60 GHz SU-MIMO testbed
We introduce a 3-phase learning framework to address frequency-dependent path loss and phase misalignments

## Slide 10: Signal-Processing based CFR Fusion
Step 1 & 2: Extract CIR and Normalize
Step 3: Delay and Phase Alignment
Step 4 & 5: Comp.-wise Fusion &
CFR Reconstruction

## Slide 11: Performance of the Heuristic Algorithm
One access point (AP) and one station (STA) is considered
CFR from channel 36 and 163 are fused
The fused band is used to beamform in channel 36
We focus on domain adaptive learning-based approach
Signal-Strength-based heuristic fusion is not very robust

## Slide 12: BandWeave Walkthrough
BandWeave
Beamformer
BandWeave
Beamformee
BandWeave Beamformed Data
Pilot Frames for Band 1,2….NB
1
Estimate CFR, H(f)
Obtain CIR, H(t)
For band 1,2…NB
2
Three Phase BandWeave Learning Algorithm
3
Obtain Hfused(f) from Hfused (t)
4
Obtain Beamforming Feedback from Hfused(f)
5
Estimate Steering Matrix
Apply Precoding
6

## Slide 13: BandWeave Learning Algorithm
BandWeave Learning Algorithm
Phase 1
Supervised Pre-training
Phase 2
Simulation in the Loop Fine-tuning
Phase 3
Online Feedback Aware Adaptation

## Slide 14: Phase-1: Supervised Pre-training
CIR-Band-1
CIR-Band-NB
Per-Band Encoder
(Conv1D / Projection)
Per-Band Encoder
(Conv1D / Projection)
Token Embeddings
Token Embeddings
Concatenate +
Positional Encoding
Multi-Head Self-Attention Module
Decoder Head
Fused CIR Output
CIRs are projected into embeddings via encoder
Embeddings are concatenated and processed by multi-head self-attention module
Algorithm 1 as pseudo-ground-truth with the loss as:

## Slide 15: Phase-2 and 3: Finetuning and Online Adaptation
Fused CIR is evaluated in a full-stack simulator to obtain BER
Model parameters are fine-tuned to minimize BER
Phase 2: Finetuning through Simulation in the Loop
Phase 3: Online Feedback Aware Adaptation
Step 1: If performance is better than the baseline, apply gradient-free perturbations to refine the model
Step 2: Otherwise, fine-tune using Algorithm 1 as surrogate supervision

## Slide 16: BandWeave Experimental Setup
Evaluated BandWeave on IEEE 802.11ac MU-MIMO and mmWave SU-MIMO testbeds
Tested across LoS, NLoS, and dynamic scenarios in three environments

## Slide 17: Performance Analysis of BandWeave (1)
Achieves up to 7.5x throughput gain and 4.9x BER reduction over SOTA
Robust in non-contiguous bands, achieving up to 12.6% throughput gain and 7.1% BER reduction
Performance with Varying Channel Condition
Performance with Non-Contiguous Band

## Slide 18: Performance Analysis of BandWeave (2)
Online adaptation boosts performance by ~7 %, reaching up to 15% total throughput gain
BandWeave achieves up to 20x lower latency and 18x lower energy than SOTA (HiSAC)
Impact of Online Adaptation
Inference-time and Energy Consumption Analysis

## Slide 19: Possible Next Steps?
This work 💪
Future Directions 🚀
✅ Multi-Band Fusion within the Same Frequency Range (e.g., 5 GHz Wi-Fi bands)
⚠️ Fusion Across Different Frequency Ranges (e.g., 2.4 GHz ↔ 5 GHz ↔ mmWave)
⚠️ Generalizable channel representation

## Slide 20
BANDWEAVE: Enhanced Channel Estimation in
MIMO Networks with Multi-Band Fusion
THANK YOU
K Foysal Haque
Haque.k@northeastern.edu

## Slide 22: BandWeave Backup Slides

## Slide 23: Transformer Architecture
CIR-Band-1
CIR-Band-NB
Per-Band Encoder
(Conv1D / Projection)
Per-Band Encoder
(Conv1D / Projection)
Token Embeddings
Token Embeddings
Concatenate +
Positional Encoding
Multi-Head Self-Attention Module
Decoder Head
Fused CIR Output
Step 1: Per-Band Encoding → We input CIRs from multiple bands → Each CIR is converted into tokens (delay × antenna) → encoder maps them into embeddings
Step 2: Add Structural Information → Add delay positional encoding + antenna embedding → Each token now contains signal + temporal + spatial context
Step 3: Cross-Band Concatenation → Tokens from all bands are concatenated into one sequence → Enables joint processing across frequencies
Step 4: Transformer Encoder → The concatenated tokens pass through 2 transformer layers → Each layer has: Multi-head self-attention,
Feedforward network

## Slide 24: Transformer Architecture
CIR-Band-1
CIR-Band-NB
Per-Band Encoder
(Conv1D / Projection)
Per-Band Encoder
(Conv1D / Projection)
Token Embeddings
Token Embeddings
Concatenate +
Positional Encoding
Multi-Head Self-Attention Module
Decoder Head
Fused CIR Output
Per-Band Encoder (Projection Layer) → Conv1D / Linear projection + activation (ReLU) → Purpose: map CIR components → embedding space
Transformer Encoder (Cross-Band Learning)
→ 2 Transformer encoder layers → Each layer consists of:
Multi-head self-attention
Feedforward network (FFN)
Decoder
→ 2-layer MLP

## Slide 25: Covariance Matrix Adaptation Evolution Strategy (CMA-ES)
1. Initialize search
Start from current parameter estimate
Define a search distribution (center + spread)
2. Generate population
Sample multiple candidate parameter sets around the current estimate
Each candidate = a slightly perturbed model
3. Evaluate fitness
Compute objective (e.g., validation loss) for each candidate
4. Select best candidates
Keep top-performing solutions
Discard low-performing ones
5. Update search distribution
Shift the center toward better candidates
Adapt the search shape to:
  emphasize directions that improved performance
  reduce exploration in poor directions
6. Iterate
Repeat sampling → evaluation → update
Gradually converges to optimal parameters

## Slide 26: Performance Analysis of BandWeave (3)
Performance with Heterogenous Bands
2 band vs 3 band Fusion Performance

## Slide 27: Additional Slides

## Slide 28: Compressing CFR with SVD
The CFR is a 𝐾×𝑀×𝑁
matrix 𝐇 for each beamformee
𝐔𝑘 and 𝐙𝑘 are 𝑁×𝑁 and 𝑀×𝑀 unitary matrices,
while the singular values are collected in the 𝑁×𝑀 diagonal matrix 𝐒𝑘
𝐕𝑘 is defined by collecting the first 𝑁SS ≤ 𝑁 columns of 𝐙𝑘

## Slide 29: Compressing CFR with SVD

## Slide 30: BFAs vs MU-MIMO Config

## Slide 31: LTF Equation

## Slide 32: CFR Equation

## Slide 33: CFR Equation

## Slide 34: CIR Equation

## Slide 35: From CFR to BFI
MU-MIMO Beamformer
Null Data Packet (NDP)
Beamforming Feedback Information
MU-MIMO Beamformees
Estimate CFR, H
Compress CFR, Vk
Create BFI Frame
1
2
3
4

## Slide 36: Beamforming feedback matrices
Transmitted unencrypted
Packet Bytes