## Slide 1
BeamID: Domain-Adaptive Radio Fingerprinting
with MIMO Beamforming Feedback
K Foysal Haque*†, Francesca Meneghello*, Francesco Restuccia*
*Institute for Intelligent Networked Systems, Northeastern University, Boston, USA
†IMDEA Networks Institute, Madrid, Spain

## Slide 2: The Era of Massive Connectivity
Number of the connected devices predicted to reach 39 Billion by 2030
1. State of IoT 2025: Number of connected IoT devices growing 14% to 21.1 billion globally “https://iot-analytics.com/number-connected-iot devices/ ”
Today’s Digital World Runs on 21+ Billion Connected Devices [1]

## Slide 3: What are the Implications?
We need to reliably identify and authenticate
devices at the physical layer
Spectrum
Management
Network
Policies
Security
Concerns

## Slide 4: Radio Fingerprinting for Authentication
Radio Fingerprinting is a promising alternative to cryptographic authentication
STA 2
Access point (AP)
Hardware Imperfections Percolate to Signal
Authentication
of the STA
STA 1
Notes: Cryptographic-based authentication has long been the standard for security. However, it requires key management and additional communication and computation overhead. Furthermore, if a device’s secret key is compromised, the attacker can successfully impersonate that device. These limitations have motivated radio fingerprinting as a promising alternative to cryptographic authentication

## Slide 5: What has been Done so Far ? (1)
STA 2
Access point (AP)
STA 1
Extract CFR or I/Q
Authenticate
STA
DNN Model
CFR and I/Q based fingerprinting are few of the popular choices
Kong, R. and Chen, H., 2024. DeepCRF: Deep learning-enhanced CSI-based RF fingerprinting for channel-resilient WiFi device identification. IEEE Transactions on Information Forensics and Security, 20, pp.264-278.
Kong, R. and Chen, H., 2024. CSI-RFF: Leveraging micro-signals on CSI for RF fingerprinting of commodity WiFi. IEEE Transactions on Information Forensics and Security, 19, pp.5301-5315.
Restuccia, F., D'Oro, S., Al-Shawabka, A., Belgiovine, M., Angioloni, L., Ioannidis, S., Chowdhury, K. and Melodia, T., 2019, July. DeepRadioID: Real-time channel-resilient optimization of deep learning-based radio fingerprinting algorithms. In Proceedings of the twentieth ACM international symposium on mobile ad hoc networking and computing (pp. 51-60).
Requires specialized hardware / firmware support

## Slide 6: What has been Done so Far ? (2)
STA 2
AP
STA 1
Beamforming Feedback Info. (BFI)
Over-the-air BFI capture
DNN Model
Authenticate
STA
Meneghello, F., Rossi, M. and Restuccia, F., 2022, July. DeepCSI: Rethinking Wi-Fi radio fingerprinting through MU-MIMO CSI feedback deep learning. In 2022 IEEE 42nd International Conference on Distributed Computing Systems (ICDCS) (pp. 1062-1072). IEEE.
Meneghello, F., Haque, K.F. and Restuccia, F., 2025, May. Radio Fingerprinting of Wi-Fi Devices Through MIMO Compressed Channel Feedback. In IEEE INFOCOM 2025-IEEE Conference on Computer Communications Workshops (INFOCOM WKSHPS) (pp. 1-6). IEEE.
Cannot generalize to unseen domains
BFI based fingerprinting doesn’t need specialized firmware / hardware

## Slide 7: Preli. Analysis on Domain Generalization
5 diff. location for each NIC
Spacing of 4 inch between two diff. NIC loc.
AP
Performed fingerprinting to identify 15 different
NICs with BFI using VGG based model
Domain shift is a fundamental challenge
in radio fingerprinting

## Slide 8: BeamID: Domain-Adaptive RFP with BFI
Train and Test in Same Domain
Train and Test in Different Domain
Inference
Train
Domain 1
Domain 2

## Slide 9: Summary of Contributions
We propose BeamID, a domain-adaptive RFP framework that exploits MIMO beamforming feedback
We introduce an embedding-based few-shot adaptation strategy built upon supervised contrastive learning to support domain adaptation
We validate BeamID with extensive experiments with a Wi-Fi testbed, with 15 different NICs at each of 9 distinct locations
BeamID takes only 5 target-domain (unseen) samples per client, achieving up to 99% accuracy while requiring only 2.3 seconds of adaptation time

## Slide 10: From CFR to BFI
MU-MIMO Beamformer
Null Data Packet (NDP)
Beamforming Feedback Information
MU-MIMO Beamformees
Estimate CFR, H
Compress CFR, Vk
Create BFI Frame
1
2
3
4

## Slide 11: Beamforming feedback matrices
Transmitted unencrypted
Packet Bytes

## Slide 12: BeamID Walkthrough
BeamID Dataset Creation
6
BeamID Model training
7
MU-MIMO Beamformer
Null Data Packet (NDP)
Beamforming Feedback Information
MU-MIMO Beamformees
Estimate CFR
Compress CFR
Create BFI Frame
1
2
3
4
Feedback Frame Capture with
Wi-BFI [1]
5
If Switching to
A new domain
1. Haque, K.F., Meneghello, F. and Restuccia, F., 2023, October. Wi-BFI: Extracting the IEEE 802.11 beamforming feedback information from commercial Wi-Fi devices. In Proceedings of the 17th ACM Workshop on Wireless Network Testbeds, Experimental evaluation & Characterization (pp. 104-111).
BeamID
Inference
8
Domain Adaptation
9

## Slide 13: Source-Domain Representation with Embedding
V matrices
Data Aggregation
Encoder
V-matrix Tensor
Shape: (B × 16 × 250)
1D Convolution Block 1
Conv1D (32),
Batch Normalization,ReLU
1D Convolution Block 2
Conv1D (32),
Batch Normalization,ReLU
1D Convolution Block 3
Conv1D (32),
Batch Normalization,ReLU
Global Average Pooling
AdaptiveAvgPool1D →
(B × 128)
Output Embedding 𝒛 ∈ ℝᵈ
(d = 128)

## Slide 14: Enabling Domain Invariant Features
We employ Supervised Contrastive loss, which directly enforces intraclass compactness and inter-class separation-properties
Numerator pulls same-client embeddings together, whereas, Denominator contrasts against all other embeddings in the batch
To enable device identification during training, the contrastive objective is combined with a standard cross-entropy loss
The overall training objective

## Slide 15: Impact of Super Contrastive Learning
Train and Tested in the same domain
BeamID and SOTA approach-– both achieves ~99%
Train and Tested in the different domain
DeepCSIv2’s performance is random
BeamID is not totally random but still very poor

## Slide 16: Few-Shot Domain Adaptation in Embedding Space
Collect K-shot labeled target samples
Fine-tune classifier + last encoder layer
Align target embeddings with source clusters
Preserve inter-client separation
Ds
Zs
f(.)
Dkt
Zt ≈ Zs
Fine-tune

## Slide 17: Experimental Evaluation
Evaluate BeamID with WiSEC testbed, a large-scale multi-NICs platform
Hosts 15 intel AX210 Wi-Fi NIC implementing IEEE 802.11ax.
Used ASUS RT-AX86U as AP
9 diff. loc. for each NIC
Spacing of 4 inch between two diff. NIC loc.
Access Point
Wi-Fi NICs
Testbed Setup
NIC Antenna
NIC 1
NIC 15

## Slide 18: BeamID Performance (1)
Performance with domain adaptation
Pairwise cross-domain transfer accuracy at k = 15
Legends show the training domain
Tested with rest of the domain

## Slide 19: BeamID Performance (2)
Experimental Scenarios with Training and Testing Locations
Accuracy vs number of source environments
Impact of fine-tuning the encoder

## Slide 20: Computational Overhead of BeamID
Executed BeamID in a linux machine with intel core i7-12700K CPU
and RTX A4000 GPU with 84 GB RAM
BeamID takes only 133 ms for inference time whereas it takes up to 2.32 s
for adapting to an unseen domain

## Slide 21: Possible Next Steps?
This work 💪
Future Directions 🚀
✅ Few-shot cross-domain RFP from standard MIMO beamforming feedback
⚠️ Extend BeamID across heterogeneous AP hardware
⚠️ Generalize BeamID across different frequency bands

## Slide 22
BeamID: Domain-Adaptive Radio Fingerprinting
with MIMO Beamforming Feedback
THANK YOU
K Foysal Haque
Haque.k@northeastern.edu

## Slide 23: Controller-level integration of BeamID