## Slide 1
K. Foysal Haque
MENTIS Lab
Institute for the Wireless Internet of Things (WIoT)
Northeastern University
Beamsense: Rethinking Wireless Sensing with MU-MIMO Wi-Fi Beamforming Feedback

## Slide 2: AR/VR: Shaping the Future of Interactions
We are very far from truly seamless and immersive
AR/VR experiences
1. Precedence Research. "Spatial Computing Market Size, Share, Trends, Analysis Report, 2025-2034." Accessed October 21, 2025. https://www.precedenceresearch.com/spatial-computing-market
Global market value is predicted to reach 1066 Billion by 2034 [1]

## Slide 3: What is the Current Bottleneck?
Semantic segmentation
Object recognition​
Compute-intensive
AI/ML tasks
120 Hz frame rate and 8K resolution are needed! [1]
1. M Gallagher, ER Ferrè, "Cybersickness: a multisensory integration perspective", Multisensory Research, 2018. Ars Technica, "Virtual Perfection: Why 8K resolution per eye isn't enough for perfect VR", 2013.

## Slide 4: State of Current Wireless AR/VR Headsets
Meta Quest 3
1.5-2 hours
Weight
515 grams
Refresh rate
Up to 90 Hz
Apple Vision Pro
Up to 2 hours
Weight
650 grams plus
353 grams battery
Refresh rate
Up to 90 Hz
Controllers
External
battery

## Slide 5: Wireless Edge Computing and Sensing
Offload intensive compute task to edge server
Wireless sensing for surrounding awareness
Light-weight & device free
AR/VR experience

## Slide 6: Introduction on Wireless Sensing
Perceived by the changes in the received signal
Main approaches [1] are based on:
  Received Signal Strength
  Passive Wi-Fi Radar
  Channel Frequency Response (CFR)
Transmitted Wi-Fi
Signals
Received
Wi-Fi Signals
Channel Information
Feature Extraction
Classification
Activity
Recognition
Health Monitoring
Presence Detection
1. Khandaker Foysal Haque, Milin Zhang, Francesca Meneghello, and Francesco Restuccia. "Beamsense: Rethinking wireless sensing with mu-mimo wi-fi beamforming feedback." Computer Networks 258 (2025): 111020.

## Slide 7: Prior Work and Existing Challenges
Bahadori, N., Ashdown, J. and Restuccia, F., 2022, June. ReWiS: Reliable Wi-Fi sensing through few-shot multi-antenna multi-receiver CSI learning. In 2022 IEEE WoWMoM (pp. 50-59).
Meneghello, D. Garlisi, N. Dal Fabbro, I. Tinnirello, and M. Rossi, “SHARP: Environment and Person Independent Activity Recognition with Commodity IEEE 802.11 Access Points,” IEEE TMC, 2022.
R. Xiao, J. Liu, J. Han, and K. Ren, “OneFi: One-Shot Recognition for Unseen Gesture via COTS WiFi,” in Proceedings of the ACM Conference on Embedded Networked Sensor Systems (SenSys), pp. 206–219, 2021
Yin, G., Zhang, J., Shen, G. and Chen, Y., 2022. FewSense, towards a scalable and cross-domain Wi-Fi sensing system using few-shot learning. IEEE TMC, 23(1), pp.453-468.
Ma, Y., Zhou, G., Wang, S., Zhao, H. and Jung, W., 2018. SignFi: Sign language recognition using WiFi. Proceedings of the ACM IMWUT, 2(1), pp.1-21.
Need Firmware Modifications
Need Dedicated CSI Tools
802.11n CSI Tool
Limited Hardware
Can’t Generalize Domains

## Slide 8: BeamSense: Overview and Novelties
Requires specialized equipment
Requires Direct Access to Devices
Introduces additional overhead
Access
Point
CSI
Collectors
CSI
CSI
Existing CFR based Approaches
No specialized equipment
No Direct Access Required
No additional overhead
Access
Point
MU-MIMO Beamformees
Beamforming Feedback
BeamSense- based on BFI

## Slide 9: From CFR to BFI
MU-MIMO Beamformer
Null Data Packet (NDP)
Beamforming Feedback Information
MU-MIMO Beamformees
Estimate CFR, H
Compress CFR, Vk
Create BFI Frame
1
2
3
4

## Slide 10: Beamforming feedback matrices
Transmitted unencrypted
Packet Bytes

## Slide 11: Operation of BeamSense
AP
IEEE 802.11 ac/ax stations
STA 1
STA 2
STA N
...
...
IEEE 802.11ax
IEEE 802.11ax
IEEE 802.11ac
Woks with any device supporting MIMO
Support across multiple standard
Works with multiple bands simultaneously
No direct access to the network needed
Can be collected with a single capture
BW: 80 MHz
BW: 160 MHz
BW: 40 MHz
Edge Server

## Slide 12: Capture BFI with Wi-BFI Tool
MU-MIMO Beamformer
Null Data Packet (NDP)
Beamforming Feedback Information
MU-MIMO Beamformees
Estimate CFR
Compress CFR
Create BFI Frame
1
2
3
4
Feedback Frame Capture with
Wi-BFI [1, 2]
5
Wi-BFI captures the beamforming feedback packet
Decode the Wi-Fi BFAs based on the network configuration
Supports both online and offline extraction for IEEE 802.11ac and 802.11ax
Khandaker Foysal Haque, Francesca Meneghello, and Francesco Restuccia. "Wi-BFI: Extracting the IEEE 802.11 beamforming feedback information from commercial Wi-Fi devices." In Proceedings of the 17th ACM Workshop on Wireless Network Testbeds, Experimental evaluation & Characterization, pp. 104-111. 2023.
https://github.com/kfoysalhaque/Wi-BFI

## Slide 13: BeamSense Walkthrough
BeamSense Dataset Creation
Classification
output
BeamSense Model training
BeamSense
Inference
6
7
8
MU-MIMO Beamformer
Null Data Packet (NDP)
Beamforming Feedback Information
MU-MIMO Beamformees
Estimate CFR
Compress CFR
Create BFI Frame
1
2
3
4
Feedback Frame Capture with
Wi-BFI [1, 2]
5

## Slide 14: Data Preprocessing
Beamforming
angles extraction
S BFI packets collection
Data aggregation
(S x K x A x U)
Input Tensor
S: no. samples
K: no. OFDM sub-channels
A: no. BFI angles in a packet
U: no. MU-MIMO users
BFI packets in a window
BFI, STA #1, t = 0.001
BFI, STA #3, t = 0.086
BFI, STA #1, t = 0.095
...
Browsing phone
Walking
Sub-channels
Sub-channels
Each sample captures the variations of Angle 1 over subcarriers (234) and time (0.1s)

## Slide 15: Data Collection Campaign
Data collection campaign is done with 3 different persons, with 20 activities each in 3 different environment
Data has been collected with 3 different orientations at different times of day
Video Streams has been recorded as ground truth

## Slide 16: Experimental Testbeds
Access
Point
Station
Living Room
Kitchen
Classroom
CSI Access
Point
CSI
Monitor
BeamSense STA:
Netgear X4S AC2600
CSI Monitor:
ASUS AC86U
Standard: IEEE 802.11ac
MU-MIMO Config: 3 X 3
Channel BW: 80 MHz

## Slide 17: Performance with CNN Baseline
The baseline CNN consists of three conv-blocks with 128, 64 and 32 filters
VGG-based CNN [1]
Input
Conv-block
128
MaxPool
Flatten
Conv-block
64
Conv-block
32
Softmax
Activity label
Conv2D
Conv2D
Batch Normalization
Conv-block
ReLU
BeamSense improves the performance by 11%, compared to SOTA
The accuracy decreases by only 4.52% switching from 234 to 20 sub-channels
1. Simonyan, Karen, and Andrew Zisserman. "Very deep convolutional networks for large-scale image recognition." arXiv preprint arXiv:1409.1556 (2014).
CNN cannot generalize to new domains

## Slide 18: Meta-Learning through Few-shots
Find common features among different tasks
Meta-learning is the warm-up phase before learning
Fine-tuning on a specific task is faster with meta-learned weights
A. Nichol, J. Achiam, and J. Schulman, “On first-order meta-learning algorithms,” arXiv preprint arXiv:1803.02999, 2018
𝞱
𝞱’
𝞱*1
𝞱*2
𝞱*3
𝜏1
𝜏2
𝜏3
Meta-Learning
Adaptation

## Slide 19: FAMReS: Fast and Adaptive Micro Reptile Sensing
Due to infinite number of tasks Reptile can’t be directly adopted
We consider each batch of training data as a new task in meta-learning
𝜏2
𝜏3
𝜏4
𝜏n
𝞱
Batches
𝞱’
𝜏1
we only use a small portion of data in meta-learning and micro-learning for domain adaptation

## Slide 20: Performance of Domain Adaptation
FAMReS improves cross-environment and cross-subject accuracy by up to 35%
From 30s to10s of data from new Env.
, FAMReS accuracy drop by only 5.30%
20 GFLOPs of computation with
20 ms of inference time

## Slide 21: Key Findings
Beamsense: Rethinking Wireless Sensing with MU-MIMO Wi-Fi Beamforming Feedback
  No hardware specific firmware, or firmware modification needed
  Data Extraction can be performed with any Wi-Fi compliant device
  No dedicated extraction tool needed with tight synchronization
  Can generalize to new environments, subjects or orientations

## Slide 22: Future Work
  Sensing without no additional data at all from new environment
  Sensing with larger band to have more sensing granularity

## Slide 23
Thank You