## Slide 1
K F Haque*, Justin Kong †, Terrence J. Moore †, Francesco Restuccia*, Fikadu T. Dagefu
*Institute For the Wireless Internet of Things, Northeastern University, Boston, USA
DEVCOM Army Research Laboratory
DEER: Simultaneous Multi-Modal
Decentralized Energy Efficient Covert Routing

## Slide 2
Client
Agent
Ensuring Resiliency and Security of Wireless Networks
Is of Paramount Importance
Covert communication aims to evade detection by adversary
Covert networks need to meet a multitude of conflicting requirements

## Slide 3
Modality 1
Modality 2
Modality 3
State of the art single-modal covert routing is inefficient
Most works are based on single modality
Doesn’t fully exploit the diversity of the HetNets
High Energy Consumption
Low Throughput

## Slide 4
DEER: Simultaneous Multi-modal Decentralized
Energy Efficient Routing
DEER aims to minimize combined transmit power while maintaining throughput and covertness
High Throughput
Low Energy Consumption

## Slide 5
Novel Contributions of DEER
DEER Leverages simultaneous multi-modal transmissions
Minimizes total end-to-end transmit power through node-level and network-level optimization.
Maintains user-required constraints on throughput and covertness.
Enables decentralized, energy-efficient routing using local information.

## Slide 6
Intuition Behind DEER
Throughput depends on channel conditions
It has a non-linear relationship with transmit power
DEER Optimally leverages multiple modalities simultaneously to achieve higher throughput with lower energy consumption

## Slide 7
Proof of simultaneous multi-modal transmission being more energy efficient
Covertness threshold = 0.5 and Throughput threshold = 40 Mbps
Simultaneous multi-modal approaches take least transmission power while achieving same throughput and DEP (single hop test)

## Slide 8
DEER aims to minimize the end-to-end total transmit power of the whole route in a decentralized fashion
It also maintains the constraints on end-to-end throughput and per-hop detection error probability (DEP)
End-to-end transmit power
Per-hop DEP
DEER Overview
End-to-end throughput

## Slide 9
Signal Model
Signal is transmitted from Transmitter Th to Receiver Rh for the hop h of the whole route ψ where Willie W is the adversary. Here mk = { m1 , m2}
Rcv signal
Tx Power
Tx data
AWGN noise
Channel

## Slide 10
Network Metrics
Throughput for modality
m and hop h
Overall E2E throughput
Combined Tx Power of hop h
E2E throughput for modality
E2E Tx Power

## Slide 11
Detection at Willie
Willie perform separate hypothesis for each modality. For each modality, Willie has null hypothesis, H0 (no transmission) and and alternative hypothesis, H1 (transmission exists).
Willie calculate the average RSS for L channel uses and perform threshold check
denotes the detection threshold for modality {a, b}, and D0 and D1 denote decisions in favor of H0 and H1 for modality {a, b } and hop h

## Slide 12
Detection at Willie
The associated detection error probabilities (DEPs) for each threshold test are defined as:
Willie then combines the decision obtained for each modality
Probability of missed detection and the probability of false alarm for the overall decision

## Slide 13
Per hop Covertness in terms of Detection Error Probability
Alice tosses an unbiased coin to decide whether to transmit or not
Therefore Alice transmits with equal a priori probabilities of 1/2
PDEP of the hop h

## Slide 14
DEER solves the formulated optimization problem with node-level and network-level optimization strategies
End-to-end transmit power
Per-hop DEP
Let’s Recap the Problem Formulation
End-to-end throughput
DEER Optimization Problem

## Slide 15
DEER Algorithm : Node Level Optimization
Minimizes total transmit power (Ph​) while ensuring throughput and covertness constraints
Chooses the best modality combination for each neighbor

## Slide 16
DEER Algorithm : Network Level Optimization
Initializes D-LSRP by broadcasting LSAs with outgoing links and transmission powers
Builds LSDB by collecting LSAs to construct the network topology
Finds the minimum power route using Dijkstra’s algorithm
Updates transmission costs iteratively to minimize end-to-end power consumption

## Slide 17
Simulation Scenario of DEER
3D Simulation Setup:
Dimensions: 250 × 250 × 9.5 m³
Obstacles: Multiple concrete buildings (green cuboids)
Nodes: 36 transceiver nodes (red cones) equipped
with vertically polarized short dipole antennas at 3 m height
Communication Modalities:
Frequencies: 400 MHz, 900 MHz, and 2.4 GHz
Channel Estimation: Conducted using EM.CUBE ray tracing

## Slide 18
DEER Vs single-modal approaches
DEER Vs naive multi-modal approaches
Improves energy consumption
by up to 23.5x
Improves energy consumption
by up to 1.5x
End-to-end total transmit power as a function of Willie’s X coordinates with
Preq DEP,h = 0.5; Ureq = 30 Mbps; Modality BW: 3 MHz
DEER as a Function of Willie’s Location (1)

## Slide 19
DEER Vs single-modal approaches
DEER Vs naive multi-modal approaches
Improves energy consumption
by up to 16x
Improves energy consumption
by up to 1.5x
End-to-end total transmit power as a function of Willie’s X coordinates with
Preq DEP,h = 0.5; Ureq = 30 Mbps; Modality BW: 1% of center freq.
DEER as a Function of Willie’s Location (2)

## Slide 20
DEER as a Function of Required Throughput
User defined per hop covertness: Preq DEP,h = 0.5
DEER Vs single-modal approaches
DEER Vs naive multi-modal approaches
improves energy consumption by up to 15x

## Slide 21
Summary of Key Contributions
We introduce DEER, a decentralized energy-efficient covert routing strategy
It is the first covert routing approach to leverage multiple wireless modalities simultaneously
It improves the energy efficiency by up to 23.5%

## Slide 22
Possible Next Steps?
This work 💪🏻
Things
to do 😅
⚠️ Reduce Routing Data Overhead
⚠️ Scale the System to N number of simultaneous modalities