## Slide 1
MAGIC: Meta-Learning Adaptive Gesture Recognition with mmWave MIMO CSI
K Foysal Haque, K M Rumman, Arman Elyasi, Francesca Meneghello, Francesco Restuccia
Institute for the Wireless Internet of Things (WIoT)
Northeastern University
IEEE WoWMoM 2025

## Slide 2: Agenda
Introduction
Contribution
Related Work
System Workflow
Preprocessing
Adaptation Process
Setup
Results
Conclusions

## Slide 3: AR/VR Applications
Demanding higher data rates to support AR/VR applications

## Slide 4: What are the bottlenecks?
120 Hz @ 8K 40 Gbps WiFi supports 1.2 Gbps
LARGER AND RELIABLE BANDWIDTH IS NEEDED!!!
mmWave spectrum is the choice.

## Slide 5: mmWave Spectrum
Human Activity Classification [1, 2]
Gesture Recognition [3, 4]
Intrusion Detection [5]
Patient Monitoring [6]
Offers substantial bandwidth
More precise wireless sensing capabilities
[1] Haque, K.F., Zhang, M. and Restuccia, F., 2023, June. Simwisense: Simultaneous multi-subject activity classification through wi-fi signals. In 2023 IEEE 24th International Symposium on a World of Wireless, Mobile and Multimedia Networks (WoWMoM) (pp. 46-55). IEEE.
[2] Haque, K.F., Zhang, M., Meneghello, F. and Restuccia, F., 2025. Beamsense: Rethinking wireless sensing with mu-mimo wi-fi beamforming feedback. Computer Networks, 258, p.111020.
[3] Yu, J.T., Tseng, Y.H. and Tseng, P.H., 2024. A mmWave MIMO radar-based gesture recognition using fusion of range, velocity, and angular information. IEEE Sensors Journal, 24(6), pp.9124-9134.
[4] Xu, L., Wang, K., Gu, C., Guo, X., He, S. and Chen, J., 2024, July. GesturePrint: Enabling user identification for mmWave-based gesture recognition systems. In 2024 IEEE 44th International Conference on Distributed Computing Systems (ICDCS) (pp. 1074-1085). IEEE.
[5] Cenkeramaddi, L.R., 2023. Recent Advances in mmWave-Radar-Based Sensing, Its Applications, and Machine Learning Techniques: A Review.
[6] Pan, P., Zhang, F., Zhou, A., Ma, H. and Jia, H., 2024, July. mmCare: A Nursing Care Activity Monitoring System via mmWave Sensing. In Proceedings of the ACM Turing Award Celebration Conference-China 2024 (pp. 18-22).
{

## Slide 6: Contributions
Developed adaptive temporal embedding network for efficient long-range temporal feature extraction
Evaluated through a wide range of subjects and environments
Proposed MAGIC, a novel gesture recognition system

## Slide 7: Previous Work
mTransSee [1]
Transfer-Learning Approach
77-81GHz
3 * 4 Communication System
Gesture-mmWAVE [2]
Transformer Network
77 GHz
2 * 4 Communication System
[1] Jin, B., Ma, X., Hu, B., Zhang, Z., Lian, Z. and Wang, B., 2024. Gesture-mmWAVE: Compact and accurate millimeter-wave radar-based dynamic gesture recognition for embedded devices. IEEE Transactions on Human-Machine Systems.
[2] Liu, H., Cui, K., Hu, K., Wang, Y., Zhou, A., Liu, L. and Ma, H., 2022. mTransSee: Enabling environment-independent mmWave sensing based gesture recognition via transfer learning. Proceedings of the ACM on Interactive, Mobile, Wearable and Ubiquitous Technologies, 6(1), pp.1-28.

## Slide 8: MAGIC vs Existing mmWave Radar-based system

## Slide 9: System Workflow
Step 1
NDP
Step 2
Step 3
Detected Gesture

## Slide 10: Domain-adaptive Preprocessing Pipeline (DAPP) (1)
CFR Matrix
Attenuation Factor
Frobenius norm
Path Loss Compensation
Frequency Normalization
Entropy-Guided Filtering

## Slide 11: Domain-adaptive Preprocessing Pipeline (DAPP) (2)

## Slide 12: Data Augmentation
Scaling Factor
Random Phase Shift
Noise Addition
Scaling
Phase Perturbation

## Slide 13: Adaptive Temporal Embedding Network (ATEN)
Generalizing across Environments
Feature Encoding with TCNs
Task Embedding
Query-specific Adaptation and
Classification
Meta-learning-driven Adaptation

## Slide 14: Feature Encoding with TCNs
Encode temporal patterns from mmWave CFR sequences
Capture both short- and long-term dependencies in gesture dynamics
Generate compact and informative feature vectors for classification
Temporal Convolutional Network (TCN)

## Slide 15: Task Embedding
Summarize the essence of a task using its support examples
Enables the model for adaptation to new and unseen tasks
Core idea
A feature extractor processes each input to a latent vector
Vectors are aggregated into a single task embedding
Refinement

## Slide 16: Query-Specific Adaptation and Classification
Adapts query features using task embedding to align with task-specific context
Combines query representation and task summary through a learnable transformation
Produces a context-aware embedding tailored to the current task
Adapted features are passed to a classifier

## Slide 17: Meta-learning-driven adaptation
Training the model for generalization
Using cross-entropy loss on query samples
Optimizes feature extractor, task embedding and classifier using gradient descent
Aggregates losses for forming a unified meta-loss

## Slide 18: Experimental Setup [1]
Multiplexing and Diversity Gain
Digital Beamforming
P2P, SU-MIMO, MU-MIMO
Operating in 57-64 GHz
1 GHz of bandwidth
OFDM
[1] Haque, K.F., Meneghello, F., Rumman, K.M. and Restuccia, F., 2024, December. m3MIMO: An 8× 8 mmWave Multi-User MIMO Testbed for Wireless Research. In Proceedings of the 30th Annual International Conference on Mobile Computing and Networking (pp. 1922-1929).

## Slide 19: Data Collection
50 repetitions of each gesture per subject, with each lasting 3 seconds

## Slide 20: Performance Evaluation
Baselines
[1] Li, Y., Zhang, D., Chen, J., Wan, J., Zhang, D., Hu, Y., Sun, Q. and Chen, Y., 2022, December. DI-gesture: Domain-independent and real-time gesture recognition with millimeter-wave signals. In GLOBECOM 2022-2022 IEEE Global Communications Conference (pp. 5007-5012). IEEE.
[2] Hayashi, E., Lien, J., Gillian, N., Giusti, L., Weber, D., Yamanaka, J., Bedal, L. and Poupyrev, I., 2021, May. RadarNet: Efficient gesture recognition technique utilizing a miniature radar sensor. In Proceedings of the 2021 CHI Conference on Human Factors in Computing Systems (pp. 1-14).
DI-Gesture [1]
Incorporates Dynamic Range Angle Images (DRAI) and basic data augmentation
RadarNet [2]
Processes range-Doppler maps for spatial-temporal motion

## Slide 21: Results
MAGIC outperforms the SOTA Models with the average of 24.13% across all the environments
Accuray of gesture recognition methods in different environments

## Slide 22: Results
Environment Generalization Performance
MAGIC outperforms ReWis and FREL by 54% and 12% respectively
MAGIC outperforms ReWis and FREL by 66% and 15% respectively

## Slide 23: Results
Subject Generalization Performance
Outperforming ReWiS and FREL by 55% and 10% respectively

## Slide 24: Conclusions
We introduced MAGIC, a novel gesture recognition framework using mmWave CSI, which eliminates the need for radar-specific hardware
Achieves high accuracy and strong generalization across different subjects and environments
A scalable, efficient and robust solution for real-world gesture recognition applications

## Slide 25
Thanks for your attention!