## Slide 1
SAWEC:
Sensing-Assisted
Wireless Edge Computing
Foysal Haque, Francesca Meneghello, Ebtidaul Karim, Francesco Restuccia
Institute for the Wireless Internet of Things (WIoT)
Northeastern University
MENTIS Group Website: http://mentislab.info

## Slide 2: AR/VR: Next Frontier in Pervasive Computing
We are very far from truly seamless
and immersive AR/VR experiences
Notes: Immersive, interactive, and persistent shared virtual experiences
Through the Metaverse, individuals will enter a space where the cyber and physical worlds converge, thus enabling new entertainment applications, providing ultra-realistic online learning experiences and transforming healthcare through remote surgery opportunities
The Metaverse will also improve sustainability by reducing work commuting and help companies reduce their carbon footprint

## Slide 3: What is the current bottleneck?
Semantic Segmentation
Object
Recognition​
Compute-Intensive
AI/ML Tasks
120 Hz frame rate and 8K resolution are needed!
M Gallagher, ER Ferrè, "Cybersickness: a multisensory integration perspective", Multisensory Research, 2018.
Ars Technica, "Virtual Perfection: Why 8K resolution per eye isn't enough for perfect VR", 2013.
Notes: to avoid pixelation and motion sickness

## Slide 4: State of current wireless AR/VR headsets
Meta Quest 3
1.5-2 hours
Weight
515 grams
Refresh Rate
Up to 90 Hz
Apple Vision Pro
Up to 2 hours
Weight
650 grams plus
353 grams battery
Refresh Rate
Up to
90 Hz

## Slide 5: Wireless Edge Computing
120 Hz → E2E latency of 8 milliseconds
...
120 Hz @ 8K → 40 Gbps → Wi-Fi supports 1.2 Gbps

## Slide 6
Prior Work
in
WEC
Frame partitioning
Downsize & Compression
DNN partitioning
Full task offloading
What Has Been Done So Far?
Z. Yang et al., “Edgeduet: Tiling Small Object Detection for Edge Assisted Autonomous Mobile Vision,” IEEE/ACM Transactions on Networking, 2022.
S. Laskaridis wt al., “SPINN: Synergistic Progressive Inference of Neural Networks Over Device and Cloud,” in Proceedings of MobiCom, 2020, pp. 1–15.
R. Xu et al., “ApproxDet: Content and Contention-Aware Approximate Object Detection for Mobiles,” in Proceedings of SenSys, 2020, pp. 449–462
W. Jiang, Z. Teng, M. Li, and L. P. Qian, “Energy-Efficient Data Compression and Resource Allocation for Edge Assisted IoT Networks,” in Proc. of ICCC, IEEE, 2023, pp. 1–6.

## Slide 7: Does Compression Degrade Performance?
Six facial emotion classes from six different subjects

## Slide 8
Does Compression Degrade Performance?
Up to 50% drop with 1/4
~30 ms compression time!

## Slide 9: SAWEC: Sensing-Assisted Wireless Edge Computing
Edge Server
Traditional WEC for High-Resolution Data
Frame Resize
Frame Partition
High-Res Partial Frames Through Sensing
SAWEC

## Slide 10: Summary of Key Contributions
We propose SAWEC, a new paradigm for wireless edge computing
E2E latency is optimized by offloading only the relevant data
SAWEC reduces the channel occupation and E2E latency by 94% and 96%
Improves the instance segmentation performance by 47%

## Slide 11: Overview of SAWEC
Task Execution at Server
3
ML
Task
walking avatar
talking avatar
ROI Offloading
2
360 Frame
ROI 1 ROI N
Edge
Server
VR
System
Sensing-Assisted
ROI Detection
0o
90o
180o
270o
360o
B1
A1
B2
A2
Find ROI with Wireless Sensing
Find Ax,Bx For all ROIN
N = 1, 2, 3, ……n
1

## Slide 12
Localization based on AoA and ToA
90o
-90o
0o
Cluster 1
Cluster 2
1
Detection of the Region of Interest (ROI)
Track Environmental Change
Through Moving Cluster
Time= 1.2 s
Cluster 1
Cluster 2
Time= 2.2 s
Cluster 1
Cluster 2
Moving Cluster
2
Find ROI based on AoA, ToA and Cluster Radius
Calculate the range of the Cluster
AoA
ToA
Calculate ROI
AoA: 40o
AoA(deg)
ToA(ns)
0o
-90o
90o
5 10 15 20
ToF: 7 ns
3

## Slide 13: Cluster Projection to Camera Ref. System (1)

## Slide 14: Cluster Projection to Camera Ref. System (2)
θ = [(∠OBD + θtx) mod 360]
Where,
  ∠OBD is AoA for camera ref. system
  θ is the object in 360 frame scale
  θtx is Wi-Fi tx in 360 frame scale
  mod represents modulo operation

## Slide 15: Experimental Setup
PicoScenes tool is used for CFR collection
360° video capture and CFR collection is synchronized
Six different tests are performed in each of two different environment: anechoic chamber and hall room
Components:
  Insta 360 camera
  Co-located IEEE 802.11ax client operating at 160 MHz

## Slide 16: SAWEC Performance
Instance segmentation mAP50−95 VS channel occupation at different α:
At α = 2 the ROI is sufficiently large, and the mAP50−95 reaches 67% with YOLOv8m
Instance segmentation mAP50−95 with different variants of YOLOv8
YOLOv8x achieves an mAP50-95 of 76% while YolactACOS and EdgeDuet achieve only 36% and 45% respectively

## Slide 17: Comparative analysis of SAWEC
Channel Occupation
The size of a 10K frame is 138.88 MB
SAWEC, YolactACOS, and EdgeDuet require 5.5 MB, 92.2 MB and 85.9 MB per frame respectively
Analysis with original (10K), and tolerable compressed (1/8) and resized images (1/2)
End-to-end Latency
At 10K resolution, SAWEC improves the latency by 94% on an average

## Slide 18: Summary of Key Contributions
We have proposed SAWEC, a new paradigm for wireless edge computing
E2E latency is optimized by offloading only the relevant data
SAWEC reduces the channel occupation and E2E latency by 94% and 96%
Improves the instance segmentation performance by 47%

## Slide 19: Possible Next Steps?
This work 💪🏻
Things
to do 😅
⚠️ Improve
localization
accuracy
⚠️ Scale the system to several moving objects

## Slide 20
Thank You
haque.k@northeastern.edu